## Slide 1: BIOMECHANICS & BIOMEDICAL ENGINEERING LOW COST FORCE SENSOR
Team members:
Gartzonikas Dimitrios
Tzortzopoulos Georgios
Mentor: Gκousioudi Anastasia - Consultant: Tzeranis Dimitrios

## Slide 2: Why? simultaneous force measurements on multiple samples What? analog input into digital output How? load change resisntance change voltage change

## Slide 3: Force sensor assembly main parts
Voltage supplies, reference, regulators
Force Sensor FSR400
Operational amplifiers
Analog to digital converter
Cables, resistances, capacitors etc.

## Slide 4: Challenges
Operational limitations of converter
Voltage supply for opamp
FSR response affected by:
- operational force range
- deformation
- load distribution on active tip
Output signal processing

## Slide 5: Practical solutions
Simulations (Tina-Ti, LT Spice)
Stable connections and mounting
Active surface in a rubber sandwich
Secondary opamp supply circuit
Controllable gain
Arduino instead of adc

## Slide 6: Theory & practice (1)
Defining the FSR’s response…
Chart: Resistance/Force Chart
| 0.1 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5
test 1 | 4000 | 170 | 110 | 62 | 45 | 38 | 30.5 | 27
test 2 | 1000 | 130 | 105 | 57 | 45.5 | 33.5 | 26 | 24 | 20.5 | 18.5 | 17.5 | 16 | 15
test 3 | 300 | 135 | 91 | 55 | 43 | 30 | 27 | 22.5 | 20 | 18 | 17 | 16 | 14.5
test 4 | 370 | 275 | 103 | 66 | 46 | 35.5 | 32 | 26 | 22 | 21.5 | 19 | 17.5
test 5 | 380 | 270 | 105 | 77 | 47 | 39 | 33 | 30.5 | 23.5 | 21.5 | 20 | 18 | 16 | 15
test 6 | 350 | 150 | 100 | 75 | 43.5 | 36.5 | 31 | 28 | 23.5 | 21.5 | 19.5 | 18 | 16.5 | 15.5
test 7 | 180 | 90 | 74 | 72 | 53 | 36 | 29 | 26 | 23.5 | 21 | 19 | 18 | 16
test 8 | 205 | 135 | 95 | 80 | 65 | 41 | 34 | 27 | 23.5 | 22.5 | 19 | 17.5 | 16.5 | 15
test 9 | 165 | 120 | 80 | 70 | 60 | 40 | 32 | 25.5 | 23 | 21 | 18 | 17 | 15.5 | 14.5
w/o discs | 22000 | 1000 | 107.4 | 70 | 50 | 38.5 | 30.5 | 27.6 | 24.5 | 21.5

## Slide 7: Theory & practice (2)
manufacturer vs. experiment…
Chart: force (g)

## Slide 8: Final design & implementation

## Slide 9: Implementation in detail
Ground
Positive
Voltage
Negative
Voltage
FSR
Input
Output to
converter

## Slide 10: Experiment layout

## Slide 11: Equipment & protocols
Equipment:
Digital polymeter
Bose test instrument
Arduino Mega
Laptop
Experiment conditions:
velocity 0,05 mm/sec
0,5 Ν force step
steady load for 30 sec
0,1 – 7,5 N load range
rubber discs Φ6x3mm
9 repetitions

## Slide 12: Assembly response
1,5 N
1,0 N
3,0 N
3,5 N
4,5 N
4,0 N
2,5 N
6,5 N
6,0 N
5,5 N
5,0 N
7,5 N
7,0 N

## Slide 13: Assembly calibration
Chart: Voltage to force Diagram
| 0.12228014823333337 | 0.226096086 | 0.35634118999999997 | 0.46495418799999999 | 0.57628251600000002 | 0.69485174999999999 | 0.78825892200000003 | 0.85831434100000004 | 0.91506460999999994 | 0.98991707900000003 | 1.0549943879999999 | 1.115817678 | 1.1502721119999999
 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5
Force | Voltage
N | V ± 0.02
1.5 | 0.12
2.0 | 0.23
2.5 | 0.36
3.0 | 0.46
3.5 | 0.58
4.0 | 0.69
4.5 | 0.79
5.0 | 0.86
5.5 | 0.92
6.0 | 0.99
6.5 | 1.05
7.0 | 1.12
7.5 | 1.15

## Slide 14: Conclusions
Reliable response range: 1,5 - 7,5 N
F = 2.8677*V^2 + 1.871*V + 1.377 [+/- 0,4 N]
Repeatability of results
Almost constant deviation for different forces
Small contribution of circuit dynamics
Limited precision
Great circuit robustness & negligible noise

## Slide 15: Next steps…
Stable multiple mounting
Circuit “clean up” for minimal space demands
Force offset layout
Sample placement with even distribution on FSR surface
Arduino code for quicker sampling response
Influence of rubber elasticity on the results

## Slide 16: Application & future use
Part of laboratory equipment for evaluating mechanical properties of cartilage samples

## Slide 17: THE END
We would like to thank our mentor and consultant for their support and guidance
Feel free to ask us any questions…

## Slide 18: Back up slides (1)
experiment measurements
…
step |  | test 1 | test 2 | test 3 | test 4 | test 5 | test 6 | test 7 | test 8 | test 9 | Average | ST. DEV.
ΑΑ | N | V |  |  | V |  |  | V |  |  | V | 
1 | 0,1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2 | 0,5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
3 | 1,0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
4 | 1,5 | 0,146628 | 0,146628 | 0,146628 | 0,146628 | 0,146628 | 0,073314 | 0,12219 | 0,097752 | 0,146628 | 0,12228 | 0,024234
5 |  | 0,12219 | 0,12219 | 0,12219 | 0,12219 | 0,12219 | 0,058651 | 0,102639 | 0,136852 | 0,12219 |  | 
6 |  | 0,14174 | 0,14174 | 0,14174 | 0,14174 | 0,14174 | 0,063539 | 0,107527 | 0,127077 | 0,14174 |  | 
7 |  | 0,12219 | 0,12219 | 0,12219 | 0,12219 | 0,12219 | 0,063539 | 0,097752 | 0,136852 | 0,12219 |  | 
8 |  | 0,14174 | 0,14174 | 0,14174 | 0,14174 | 0,14174 | 0,063539 | 0,127077 | 0,14174 | 0,14174 |  | 
9 |  | 0,12219 | 0,12219 | 0,12219 | 0,12219 | 0,12219 | 0,063539 | 0,127077 | 0,112414 | 0,12219 |  | 
10 | 2,0 | 0,210166 | 0,210166 | 0,210166 | 0,210166 | 0,210166 | 0,166178 | 0,219941 | 0,200391 | 0,210166 | 0,226096 | 0,021042
11 |  | 0,219941 | 0,219941 | 0,219941 | 0,219941 | 0,219941 | 0,185728 | 0,210166 | 0,234604 | 0,219941 |  | 
12 |  | 0,219941 | 0,219941 | 0,219941 | 0,219941 | 0,219941 | 0,195503 | 0,210166 | 0,229717 | 0,219941 |  | 
13 |  | 0,244379 | 0,244379 | 0,244379 | 0,244379 | 0,244379 | 0,200391 | 0,210166 | 0,215054 | 0,244379 |  | 
14 |  | 0,249267 | 0,249267 | 0,249267 | 0,249267 | 0,249267 | 0,195503 | 0,229717 | 0,244379 | 0,249267 |  | 
15 |  | 0,254154 | 0,254154 | 0,254154 | 0,254154 | 0,254154 | 0,190616 | 0,239492 | 0,244379 | 0,254154 |  | 
16 | 2,5 | 0,361681 | 0,361681 | 0,361681 | 0,361681 | 0,361681 | 0,293255 | 0,312805 | 0,322581 | 0,361681 | 0,356341 | 0,020655
17 |  | 0,371457 | 0,371457 | 0,371457 | 0,371457 | 0,371457 | 0,327468 | 0,317693 | 0,337243 | 0,371457 |  | 
18 |  | 0,371457 | 0,371457 | 0,371457 | 0,371457 | 0,371457 | 0,327468 | 0,347019 | 0,351906 | 0,371457 |  | 
19 |  | 0,371457 | 0,371457 | 0,371457 | 0,371457 | 0,371457 | 0,332356 | 0,347019 | 0,376344 | 0,371457 |  | 
20 |  | 0,351906 | 0,351906 | 0,351906 | 0,351906 | 0,351906 | 0,312805 | 0,342131 | 0,351906 | 0,351906 |  | 
21 |  | 0,376344 | 0,376344 | 0,376344 | 0,376344 | 0,376344 | 0,312805 | 0,347019 | 0,356794 | 0,376344 |  | 
22 | 3,0 | 0,469208 | 0,469208 | 0,469208 | 0,469208 | 0,469208 | 0,40567 | 0,464321 | 0,483871 | 0,469208 | 0,464954 | 0,013395
23 |  | 0,464321 | 0,464321 | 0,464321 | 0,464321 | 0,464321 | 0,42522 | 0,474096 | 0,464321 | 0,464321 |  | 
24 |  | 0,464321 | 0,464321 | 0,464321 | 0,464321 | 0,464321 | 0,459433 | 0,449658 | 0,488759 | 0,464321 |  | 
25 |  | 0,469208 | 0,469208 | 0,469208 | 0,469208 | 0,469208 | 0,439883 | 0,454545 | 0,469208 | 0,469208 |  | 
26 |  | 0,469208 | 0,469208 | 0,469208 | 0,469208 | 0,469208 | 0,449658 | 0,483871 | 0,493646 | 0,469208 |  | 
27 |  | 0,469208 | 0,469208 | 0,469208 | 0,469208 | 0,469208 | 0,44477 | 0,454545 | 0,469208 | 0,469208 |  | 

## Slide 19: Back up slides (2)
Gain selection diagrams
Chart: 
Chart: